Department of Computer Science and Information Systems

Birkbeck College, London

Introduction to Computer Systems

Worksheet for Week 4

4th February 2020

This worksheet contains questions for private study. It does not contribute to the assessment for Introduction to Computer Systems.

Question 1. What is gained by increasing the rotation rate of a disk or CD? (Brookshear and Brylow, Section 1.3, question 1.)

Question 2. A magnetic disk has a storage density of 15 GBit/sq cm. The disk holds 1 Terabyte on a single surface. Estimate the surface area and radius of the disk. If the data rate is 125 Megabytes/second and the rotation rate is 10,000 revs/minute, then estimate the amount of data read on one turn of the disk.

Question 3. High definition video can be delivered at a rate of 30 frames per second (fsp) where each frame has a resolution of 1920×1080 pixels using 24 bits per pixel. Can an uncompressed video stream of this format be sent over a USB 1.1 serial port? USB 2.0 serial port? USB 3.0 serial port? (Note: The maximum speeds of USB 1.1, USB 2.0, and USB 3.0 serial ports are 12 Mbps, 480 Mbps and 5 Gbps respectively. bps = bits per second.) (Brookshear and Brylow, Chapter 2, review problems number 46.)

Question 4. Suppose a person is typing forty words per minute at a keyboard. (A word is considered to be five characters.) If a machine executes 500 instructions every microsecond (millionth of a second), how many instructions does the machine execute during the time between the typing of two consecutive characters? (Brookshear and Brylow, Chapter 2 review problems number 47.)